## Slide 1: Target Detection
Hyperspectral Remote Sensing

## Slide 2
Dr. Hasanlou
810399040
aghdam.zamiri.fa@ut.ac.ir
Faezeh Zamiri
University of Tehran
College of Engineering
Faculty of Surveying and Geospatial engineering
Remote Sensing

## Slide 3: Method
General scheme of Target Detection
Hyperspectral image with N spectral bands
Read image
Target Detection
Otsu
Threshold Selection
Orthogonal Subspace Projection (OSP)
Adaptive Matched Subspace Detector (AMSD)
Compare
ROC curve
Generalized Likehood Ratio Test (GLRT)
Matched Filter
Signed Adaptive Cosine Estimator (S-ACE)
Adaptive Cosine Estimator (ACE)
Constrained Energy Minimization (CEM)

## Slide 4
Target Detection
Structured methods for target detection
Constrained Energy Minimization
(CEM)
Adaptive Cosine Estimator
(ACE)
Signed Adaptive Cosine Estimator
(S-ACE)
Matched Filter
Generalized Likehood Ratio Test
(GLRT)
4

## Slide 5: Target Detection
Unstructured methods for target detection
Adaptive Matched Subspace Detector (AMSD)
Orthogonal Subspace Projection
(OSP)

## Slide 6: Threshold Selection
Otsu
Otsu's method chooses a threshold that minimizes the intraclass variance of the thresholded black and white pixels.
1

## Slide 7: Data
Data that I used in this exercise.
The Cooke City Dataset
(280*800) *126

## Slide 8: Result of OTSU Threshold Selection
Method | Fabric 1 | Fabric 2 | Fabric 3 | Fabric 4 | Vehicle 1 | Vehicle 2 | Vehicle 3
CEM | 0.0010 | 0.0028 | 0.0035 | 0.0011 | 0.0032 | 0.0090 | 0.0012
ACE | 0.0155 | 0.0182 | 0.0183 | 0.0159 | 0.0150 | 0.0185 | 0.0164
S-ACE | 0.0135 | 0.0166 | 0.0155 | 0.0136 | 0.0122 | 0.0159 | 0.0134
MF | 0.0010 | 0.0027 | 0.0035 | 0.0011 | 0.0032 | 0.0089 | 0.0012
GLRT | 0.0154 | 0.0180 | 0.0181 | 0.0157 | 0.0149 | 0.0183 | 0.0163
OSP | 0.0026 | 0.0064 | 0.0011 | 0.0028 | 0.0068 | 0.0154 | 0.0021
AMSD | 0.0981 | 0.0783 | 0.0648 | 0.0934 | 0.0903 | 0.1622 | 0.0647

## Slide 9: Threshold Selection Result on OSP Method
Fabric 1
T = 0.0026
Vehicle 1
T = 0.0068
Fabric 4
T = 0.0028
Fabric 3
T = 0.0011
Fabric 2
T = 0.0064
Vehicle 3
T = 0.0021
Vehicle 2
T = 0.0154
This algorithm seems to work optimistically or because the amount of target data is small, this algorithm has low accuracy

## Slide 10: CEM Constrained Energy Minimization
HYPERCEM Performs constrained energy minimization (CEM) algorithm
Performs the constrained energy minimization algorithm for target detection.
  Usage
  [results] = hyperCem(M, target)
  Inputs
  M - 2d matrix of HSI data (p x N)  126*224000
  target - target of interest (p x 1)  126*1
  Outputs
  results - vector of detector output (N x 1)  224000*1
1 of 5 Structured Method

## Slide 11: ACE Adaptive Cosine Estimator
HYPERACE Performs the adaptive cosin/coherent estimator algorithm
Performs the adaptive cosin/coherent estimator algorithm for target detection.
  Usage
  [results] = hyperAce(M, S)
  Inputs
  M - 2d matrix of HSI data (p x N) )  126*224000
  S - 2d matrix of target endmembers (p x 1)  126*1
  Outputs
  results - vector of detector output (N x 1)  224000*1
2 of 5 Structured Method

## Slide 12: GLRT Generalized Likehood Ratio Test
HYPERGLRT Performs the generalized liklihood test ratio algorithm
Performs the generalized liklihood test ratio algorithm for target detection.
  Usage
  [results] = hyperGlrt(M, U, target)
  Inputs
  M - 2d matrix of HSI data (p x N)  126*224000
  t - target of interest (p x 1)  126*1
  Outputs
  results - vector of detector output (N x 1)  224000*1
3 of 5 Structured Method

## Slide 13: S-ACE Signed Adaptive Cosine Estimator (S-ACE)
HYPERACE Performs the adaptive cosin/coherent estimator algorithm
Performs the adaptive cosin/coherent estimator algorithm for target detection.
  Usage
  [results] = hyperSignedAce(M, S)
  Inputs
  M - 2d matrix of HSI data (p x N)  126*224000
  S - target of interest (p x 1)  126*1
  Outputs
  results - vector of detector output (N x 1)  224000*1
4 of 5 Structured Method

## Slide 14: MF Matched Filter
HYPERACE Performs Matched Filter estimator algorithm
Performs the estimator algorithm for target detection.
  Usage
  [results] = hyperMatchedFilter(M, S)
  Inputs
  M - 2d matrix of HSI data (p x N)  126*224000
  S - target of interest (p x 1)  126*1
  Outputs
  results - vector of detector output (N x 1)  224000*1
5 of 5 Structured Method

## Slide 15: OSP Orthogonal Subspace Projection
HYPEROSP Performs the othogonal subspace projection (OSP) algorithm
Performs the othogonal subspace projection algorithm for target detection.
  Usage
  [results] = hyperOsp(M, U, target)
  Inputs
  M - 2d matrix of HSI data (p x N)
  U - 2d matrix of background endmebers (p x q)
  target - target of interest (p x 1)
  Outputs
  results - vector of detector output (N x 1)
1 of 2 Unstructured Method

## Slide 16: AMSD Adaptive Matched Subspace Detector
HYPERAMSD Adaptive matched subspace detector (AMSD) algorithm
Performs the adaptive matched subspace detector (AMSD) algorithm for target detection
  Usage
  [results] = hyperAmsd(M, U, target)
  Inputs
  M - 2d matrix of HSI data (p x N)
  B - 2d matrix of background endmebers (p x q)
  target - target of interest (p x 1)
  Outputs
  results - vector of detector output (N x 1)
2 of 2 Unstructured Method

## Slide 17: Fabric 1
Result of Structured Method
Detector Map
CEM
ACE
S-ACE
GLRT
Matched Filter

## Slide 18: Fabric 1
Result of Unstructured Method
Detector Map
AMSD
OSP
In Unstructured method, first of all estimate number of endmembers
with HFC ,that is 36 , then calculate matrix of background endmembers with ATGP and finally use AMSD and OSP to target detection.

## Slide 19
Fabric 1
ROC curve of Fabric 1 data for 1000 different thresholds
The AUC of each curve calculated
Method | AUC
CEM | 0.987
ACE | 0.944
SACE | 0.991
MF | 0.991
GLRT | 0.944
OSP | 0.932
AMSD | 0.758

## Slide 20: Fabric 2
Result of Structured Method
Detector Map
CEM
ACE
S-ACE
GLRT
Matched Filter

## Slide 21: Fabric 2
Result of Unstructured Method
Detector Map
AMSD
OSP
In Unstructured method, first of all estimate number of endmembers
with HFC ,that is 36 , then calculate matrix of background endmembers with ATGP and finally use AMSD and OSP to target detection.

## Slide 22
Fabric 2
ROC curve of Fabric 2 data for 1000 different thresholds
The AUC of each curve calculated
Method | AUC
CEM | 0.998
ACE | 0.975
SACE | 0.998
MF | 0.999
GLRT | 0.975
OSP | 0.935
AMSD | 0.871

## Slide 23: Fabric 3
Result of Structured Method
Detector Map
CEM
ACE
S-ACE
GLRT
Matched Filter

## Slide 24: Fabric 3
Result of Unstructured Method
Detector Map
AMSD
OSP
In Unstructured method, first of all estimate number of endmembers
with HFC ,that is 36 , then calculate matrix of background endmembers with ATGP and finally use AMSD and OSP to target detection.

## Slide 25
Fabric 3
ROC curve of Fabric 3 data for 1000 different thresholds
The AUC of each curve calculated
Method | AUC
CEM | 0.970
ACE | 0.938
SACE | 0.977
MF | 0.972
GLRT | 0.939
OSP | 0.995
AMSD | 0.961

## Slide 26: Fabric 4
Result of Structured Method
Detector Map
CEM
ACE
S-ACE
GLRT
Matched Filter

## Slide 27: Fabric 4
Result of Unstructured Method
Detector Map
AMSD
OSP
In Unstructured method, first of all estimate number of endmembers
with HFC ,that is 36 , then calculate matrix of background endmembers with ATGP and finally use AMSD and OSP to target detection.

## Slide 28
Fabric 4
ROC curve of Fabric 4 data for 1000 different thresholds
The AUC of each curve calculated
Method | AUC
CEM | 0.991
ACE | 0.909
SACE | 0.991
MF | 0.991
GLRT | 0.909
OSP | 0.994
AMSD | 2
I think the Results of Unstructured method are related to number of endmembers and number of thresholds

## Slide 29: Vehicle 1
Result of Structured Method
Detector Map
CEM
ACE
S-ACE
GLRT
Matched Filter

## Slide 30: Vehicle 1
Result of Unstructured Method
Detector Map
AMSD
OSP
In Unstructured method, first of all estimate number of endmembers
with HFC ,that is 36 , then calculate matrix of background endmembers with ATGP and finally use AMSD and OSP to target detection.

## Slide 31
Vehicle 1
ROC curve of Vehicle 1 data for 1000 different thresholds
The AUC of each curve calculated
Method | AUC
CEM | 0.981
ACE | 0.926
SACE | 0.980
MF | 0.982
GLRT | 0.926
OSP | 0.522
AMSD | 0.901

## Slide 32: Vehicle 2
Result of Structured Method
Detector Map
CEM
ACE
S-ACE
GLRT
Matched Filter

## Slide 33: Vehicle 2
Result of Unstructured Method
Detector Map
AMSD
OSP
In Unstructured method, first of all estimate number of endmembers
with HFC ,that is 36 , then calculate matrix of background endmembers with ATGP and finally use AMSD and OSP to target detection.

## Slide 34
Vehicle 2
ROC curve of Vehicle 2 data for 1000 different thresholds
The AUC of each curve calculated
Method | AUC
CEM | 0.909
ACE | 0.705
SACE | 0.924
MF | 0.928
GLRT | 0.706
OSP | 0.853
AMSD | 0.778

## Slide 35: Vehicle 3
Result of Structured Method
Detector Map
CEM
ACE
S-ACE
GLRT
Matched Filter

## Slide 36: Vehicle 3
Result of Unstructured Method
Detector Map
AMSD
OSP
In Unstructured method, first of all estimate number of endmembers
with HFC ,that is 36 , then calculate matrix of background endmembers with ATGP and finally use AMSD and OSP to target detection.

## Slide 37
Vehicle 3
ROC curve of Vehicle 3 data for 1000 different thresholds
The AUC of each curve calculated
Method | AUC
CEM | 0.994
ACE | 0.988
SACE | 0.995
MF | 0.995
GLRT | 0.988
OSP | 0.814
AMSD | 0.711

## Slide 38: RX Anomaly Detection
HYPERRX RX anomaly detector
hyperRxDetector performs the RX anomaly detector
  Usage
  [result] = hyperRxDetector(M)
  Inputs
  M - 2D data matrix (p x N)  126*224000
  Outputs
  result - Detector output (1 x N)  1*224000
  sigma - Covariance matrix (p x p) 126*126
  sigmaInv - Inverse of covariance matrix (p x p)  126*126

## Slide 39
RX anomaly detection for targets (detector map)
Fabric 1
Vehicle 1
Fabric 4
Fabric 3
Fabric 2
Vehicle 3
Vehicle 2

## Slide 40: The End
Faezeh Zamiri
aghdam.zamiri.fa@ut.ac.ir
Linkedin.com/in/faezeh-Zamiri-1b51081bb
09224015584
Thank You
References for codes and all of results:
https://github.com/FaezehZamiri/TargetDetection